## Slide 1: Building Data Center Ztrip – Ride Hailing Service
Ankit Sharma
Itm 315 infrastructure and hosted services
Prof. Michael Lombardo
Spring 2018

## Slide 2: INDEX
About Ztrip – Ride Sharing
States with Tax Benefits for Data Center
Why Oregon?
Why going with Raised Floor?
Components of Data Center
Structured Cabling
Data Center Floor Plan
Cooling Mechanism For the Data Center
Green Approach for Cooling Data Center – Free Cooling
Risk Assessment for Cooling Redundancy

## Slide 3: Ztrip – Ride Sharing
Ztrip is an ride sharing and transportation network company
  Private Company – Headquartered in Prineville, Oregon
  Business operated all over the United States
One of the leader in Sharing Economy
  Competitors Uber and Lyfts
Company stores critical data for their customers, drivers and Employees
  Centralized Website
  Works on all Smartphones and Tablet platforms
  Enterprise Applications such as ERP and CRM
Company vision for building data center
  Preferred cheap rates for electricity and tax break
  Tier 4 - Need High Availability for the data center
  99.995 % uptime with N+1 redundancy.
Plan to Build – 3000 Sq. Ft Server Room

## Slide 4: States with Tax Benefits for Data Center

## Slide 5: Why Oregon?
Oregon is the third largest renewable energy producing state in the United States
  Building data center in Prineville, Oregon
  Mild Climate – Naturally Available Cool Air and Low Humidity
  Suitable for Installing Airside Economizer – Free Cooling
Average Industrial Electricity Rate
  Cheap Electricity – 6.68(Cents per kWh)
  No state sales tax for data centers
Renewable Sources of Energy available
  Wind
  Solar
  Hydro

## Slide 6: Why going with Raised Floor?
For large and mid-size data center
  Provides dedicated space for cooling channel
    Good airflow management
    Compatible with cooling infrastructure
  Flexibility for future expansion
    Hides patch cords and power cables
    Looks professional and less cluttered
    Reduce damage of accidental unplug
  Cabling easily accessible under the floor
    Free from climbing a step ladder
Downside
    Initial upfront cost
    Careful arrangement of floor tiles

## Slide 7: Components of Data Center
Server Racks: Rack Cabinet
  Dell - TrippLite Smart Rack 42-Units Enclosure
  Compatible with 19-inch rack equipment
  5-year warranty
  60 Cabinets
Server: Application Server – 4U & 1U
  Dell - PowerEdge R930 & R230 Rack Server
    2.5" Chassis with up to 4 Hard Drives
    OS – Linux Ubuntu Server Addition
    CPU - 2x Intel Xeon E7-8870 v3
    Ram – 8 GB DDR5 ,2400 Ghz
    HDD - 960GB SSD

## Slide 8
Switch - Cisco Nexus 5020
  40 Port 10 Gigabit Ethernet Switch
Power Distribution Units (PDUs)
  Eaton Power Distribution Unit (PDU)
  Integrated isolation, monitoring and distribution
  Comprehensive monitoring and connectivity options
UPS - APC Symmetra LX 12kVA
  Scalable Up to 16kVA N+1 Power
  User Replaceable Batteries
  Predictive power Failure Notification
  Secure shutdown

## Slide 9
Router
  Cisco CISCO1921/k9 Series Integrated Routers
Cables
  Copper
    TERA Category 7A - Twisted Pair Copper Cables
    Speeds up to to 10Gb/s
  Fiber optic Cabling
    XGLO Fiber Optic Cabling System
    Speeds more than 10Gb/s
Generator
  Kohler – 400RE0ZJB, 60 HZ
  Diesel Generator

## Slide 10: Structured Cabling
Under the floors installation with Raised Floor
  Power Cables
  Data Cabling
  Cooling
Electrical conduits running from Two Different PDU to the circuit panels for power redundancy.
Each Server Cabinets
  Two Electrical Circuits and two power strips
  Networking
    Fiber - Used 24 strands(12 Ports) of 50 Mm multimode Fiber
    Copper - 24 Ports of Category 7A copper
  Color Coded and Labelled wiring
  Tested with TIA/EIA 568 wiring standards
Notes: We will be using structured cabling with distributed power source for our data center to provide power redundancy
For under the floor installation with raised floor we can install power cables , data cabling and cooling all under the raised floor installation.
We have also run electrical conduits from two different PDUs so load is divided by 50-50% on each PDU and is running to to the circut panel for power redundancy
In other words, we have each server cabinets with two electrical circuit breakers and two power strips and for networking we have used fiber cable with 24 strands of 50 Mm multimode fiber and copper with 24 ports of category 7a copper
Which are colour coded and labelled wiring with are tested with TIA.EIA 568 wiring standards.

## Slide 11: Data Center Floor Plan

## Slide 12: Cooling Mechanism For the Data Center
For Raised Floor Data Center
  Chilled Water Cooling Method
  Air Side Economizer – Free Cooling
    Reduces use of Refrigeration Compressor
Cooling Redundancy
  Used 3 Air Handlers Units
  Main Power Connection for Air Handler
  Used Separate UPS & Generator Backup for HVAC, Servers and Networking Devices

## Slide 13: Green Approach for Cooling Data Center – Free Cooling
Computer Room Air Handler Units (CRAH)
  Compatible with Airside Economizers
  Uses both outside air and chilled water for cooling
    60 % Reduce Annual Electricity Consumption
    15% Reduction in PUE
Reasons for going green with Cooling Infrastructure
  Favorable climatic conditions for using natural air for cooling
  Installing Airside Economizer in new data center facility will be feasible
  Industrial Electricity is cheaper - 6.68(Cents per kWh)

## Slide 14: Air Side Economizer

## Slide 15: Risk Assessment for Cooling Redundancy
Freezing can occur once the ambient air temperature gets below 0 °C.
Full free cooling and mixed operation starts at relatively low outdoor air temperatures.
May be maintenance intensive
Not applicable in all regions

## Slide 16: References
Rogoway, M. (2018, Januarary 19). Data centers' small-town tax breaks bring Silicon Valley to rural America Retrieved from http://www.oregonlive.com/silicon-forest/index.ssf/2015/10/small-town_tax_breaks_bring_si.html
Rareshide, M. (2017, October 23). Power in the Data Center and its Cost Across the U.S. Retrieved from https://info.siteselectiongroup.com/blog/power-in-the-data-center-and-its-costs-across-the-united-states
Rogoway, M. (2011, November 19). Data centers in Oregon: High tech meets high desert (part 1 of 3) Retrieved from http://www.oregonlive.com/business/index.ssf/2011/11/data_clouds_settle_in_oregon_w.html
Energy in Oregon (n.d.) Retrieved from https://en.wikipedia.org/wiki/Energy_in_Oregon
Cisco Nexus 5000 Series Switches.(n.d.). Retrieved from https://www.cisco.com/c/en/us/products/switches/nexus-5000-series-switches/index.html
Copper Cabling Solutions for Data Centers. Retrieved from http://www.siemon.com/us/datacenter/cabling/copper.aspx
TrippLite SmartRack 42-Units Premium Enclosure. Retrieved from http://www.dell.com/en-us/work/shop/accessories/apd/a0688999?cid=302824&st=&gclid=Cj0KCQjw-uzVBRDkARIsALkZAdm-XgN52J7m9voX7E
Cisco Nexus 5000 Series(n.d.). Retrieved from http://www.router-switch.com/n5k-c5548up-fa.html?gclid=Cj0KCQjw-uzVBRDkARIsALkZAdnLKQ9oTOY9_QLuEfjouGKzLSaCzppRp0bLlwcQshdIzK4NHr9RGEAaAqMeEALw_wcB
Captial cost calculator(n.d.). Retrieved from https://www.schneider-electric.com/en/work/solutions/system/s1/data-center-and-network-systems/trade-off-tools/data-center-capital-cost-calculator/